## Slide 1
No. 235: Intelligent Recognition of Coronary Angiography by Deep Learning Technology: A Novel Computer-Aided Diagnostic System
Tianming Du1, Lihua Xie2, Xuqing Liu1, Changdong Guan2, Honggang Zhang1, Bo Xu2
1Beijing University of Posts and Telecommunications, Beijing, China;
2Fu Wai Hospital, National Center for Cardiovascular Diseases, Chinese Academy of Medical Sciences, Beijing, China
Background: Artificial intelligence (AI) has been applied successfully in various fields related to medical images. However, the use of AI-aided imaging system in percutaneous cardiovascular interventions has never been reported. We sought to utilize intelligent method to recognize coronary angiography by deep learning technology for the very first time.
Figure 1. Data for Training
Figure 2. Workflow of the CAD System
Methods: We retrospectively collected coronary angiographic images from a large center in China. 70% data were used for developing CAD algorithm, and the other 30% were used for evaluation. A convolutional neural network (CNN) was trained using angiographic images labeled with coronary artery segment, lesion location and lesion characteristics. The precision (percent of the right pixels) and recall rate (percent of retrieved relevant pixels) were used to evaluate the model, and the structure of CNN is illustrated in Figure 3.
Angiographic position | Precision | Recall
CRA | 84.3% | 79.5%
CAU | 87.4% | 64.3%
RCA | 92.8% | 80.1%
RAO_CAU | 84.3% | 60.6%
RAO_CRA | 81.9% | 65.1%
LAO_CRA | 85.9% | 77.3%
LAO | 87.8% | 72.3%
LAO_CAU | 85.3% | 56.6%
Results: 5701 images of 5050 patients are involved in our study, where 3990 images are used for training data to establish the CNN model, 2711 images for evaluation. A 10-hour computing processing is required for training. Only 50 ms is needed for imaging recognition. For detection task of lesion including diameter stenosis, calcification, thrombus, and dissection, the recall rate is 88.2%, 82.6%, 85.5%, 85.8%, respectively. For segment prediction task, the average precision and recall rates of different angiographic position are 86.3% and 78%. .
Conclusions: The study showed preliminary feasibility of deep learning technology in angiographic recognition based on CNN model. Notably, with the increase of training images putting into the network, the model is more robust with higher accuracy.
Table 1. Coronary Artery Segments
Lesion types | Recall
Stenosis | 88.2%
Calcification | 82.6%
Thrombus | 85.5%
Dissection | 85.8%
Table 2. Specific Morphology Detection
Collecting data (5701 images)
Label branches pixel by pixel
Label locations and classes
Training model
Training model
Data augmentation (translation,
rotation, scaling)
Segment Algorithm
Detection Algorithm
Testing segment model
Testing lesion detection model
Generate a treatment plan
Form the CAD System
Data desensitization
Origin image Labeled image for segment
Origin image Labeled image for detection
The rectangular box marked in the image is the location of the thrombosis lesion.
Different color in the labeled image represent different coronary artery..
Data for segment training
Data for lesion detection training
Altrous Conv
1x1 Conv
3x3 Conv
…
Image Pooling
1x1 Conv
Encoder
Unsample
Low-level Features
1x1 Conv
Concat
3x3 Conv
Decoder
Unsample
n=1000
p=74.9%
n=2000
p=78.3%
n=3000
p=80.9%
n=4000
p=83.8%
n=5000
p=86.3%
Input
Output
Figure 3. Structure of the Neural Network
Data pre-processing
Training and testing
model
Diagnosis
generating
Lesion detection
Coronary artery segment
Thrombus